Scrumpi 3 : Known Information

Sources – Tony Smith's article and pictures, JMK's document describing the machine, and the ETI October 1978 review.

Hardware

SC/MP II Processor clocked at 3.51Mhz. The Crystal is 7.02Mhz, the spec says 3.5Mhz almost certainly rounding up.

23 keys. Arranged as a block of 16, one on the right, and two on the left, one on the far left. All aligned to the bottom. The key layout is shown in the ETI review.

The 20 keys allow the input of 65 ASCII Codes (64 ASCII codes + Carriage Return/Line Feed)

Sense A is connected to the 'INT' key.
Sense B is a serial input (cassette ?)
Flag 0 inverts the screen output.
Flag 1 is the serial output (cassette ?)
Flag 2 comes to an accessible point near the keyboard marked 'DVC', and is a user output.
Sin and Sout are not connected (cassette ?)

The lower 4k only is decoded. In a fully decoded system, the upper PROM is at 7600-77FF and the 8154 is at 7F00-7FFF (see the disassembled visual code). The lower PROM must be at 0000-01FF in a full expansion otherwise it won't boot.

Memory Map

000-7FF :	1k PROM (standard) + 1k (Expansion). The PROM code shown on the advert
shows the 2nd half of the PROM in 7C0-7FF and 000-03F. This tells us that the
default 1k is split – feasible because the ROMs are 512 x 8 ROMs, and the
Expansion is 200-5FF. Detected by a $00 being present at 0200.

800-BFF :	1k Expansion RAM, because it won't fit anywhere else – not definitely
confirmed. Expansion is done in ¼k chunks (pairs of 2112 SRAMs)

Cxx	:	Keyboard input port. Bit 7 is 'Key 21 unlabelled'. Decoding is done in software
How, is unknown. “The 16 key block is used to define characters in the 64 key
ASCII set and three of the mode keys define which part of the ASCII set the
16 key block defines”. To avoid key clashes it would seem likely that Bits 4,5,6
are the Mode shift keys, and that Bits 0-3 are read on columns/rows, and it is likely
that the address read defines which column/row is being read. See 2C2-12 of the
applications handbook for an example of this system.If this is true then from a S/W
pov the functionality is the same – it is just the mode keys and the matrix that
 we don't know. There is a very lazy decode where the mode keys map straight to
ASCII except for the third :) See page 2 of the review for the layout.

Dxx	:	UART clock is 1/15th of the 15.625Khz Line Frequency 'as per the SC/MP Introkit'
The Introkit does not have a UART. It is an AY-5-1013.

E00-EFF :	256 Byte Video RAM (pair of MM2112 RAM chips)

F00-F7F :	NS8154 I/O Ports
F80-FFF :	NS8154 128 bytes RAM confirmed by Code Disassembly.

2 x 8 bit output ports are available and used (with the 128 bytes almost certainly an 8154 It says 'NS introduced in 1977 a 40 pin package with 128 bytes RAM and 2 x I/O ports …. this could only be an 8154 !)

Display of 8 x 32 characters using a 7 x 9 Font (in a 9 x 16 box). In RAM 20-5F are ASCII characters (e.g. it is a 6 bit ASCII code converted to 7 by dropping bit 7). VDU RAM Bit 7 inverts the output. SC/MP Flag 0 inverts the output again (these are all exclusive Ors). The character set is visible in the display screen. DM8678 Character Generator. (8675BWF)

Software

ASCII Code in software include the complete range 20-5F,80-FF. 00-1F are ignored except for 01 (Clear Screen) 08 (Back Space) 0D (Carriage Return / Line Feed). 04 is used as a string end marker.

The routines PUTVDU, GETKBD, PUTTTY, GETTTY, PUTART and GETART are described in the Prom A (000-1FF). This statement about code allocation isn't true, it appears to be the other way round from disassembling the displayed code.

PROMB contains examples of instructions (G)o (I)nput =(n) Store label. ?(n) Calculate relative (L)abels (H)ex dump (C)ontinue

Components

SC/MP II Processor
MM5204 (all PROMs)
2112 x 8 (1k RAM as 8 x 256 x 4, 256 byte VDU RAM as 2 x 256 x 4)
NS8154 (128 bytes and 2 x 8 bit I/O ports)
DM8678 Character Generator
AY-5-1013 UART

Keyboard

Bits 0-3 of the data specify the column (Bit 3 = 0,Bit 2 = 1,Bit 1 = 2,Bit 0 = 3) read. Bits 0-3 of the address specify the row (0 = Bit 3,4 = Bit 2,8 = Bit 1,12 = Bit 0). Active 1 select, active 1 to detect. This is entirely arbitrary as is the bit assignments below.

Type	Offset	Bit	Characters
Unshifted	$30	$00	0,1,2,3,4,5,6,7,8,9,:,;,<,=,>,?
Alpha 1	$40	$10 (4)	@,A-O
Alpha 2	$50	$20 (5)	P-Z,[,\,],^,_
Punc	$20	$40 (6)	Space and punctuation

To convert case:

	Unshifted	Alpha 1	Alpha 2	Punc
Read Bits 4-6 :	$00	$10	$20	$40
Xor $40	$40	$50	$60	$00
Set to $30 if Zero.	$40	$50	$60	$30
Add $F0	$30 (0)	$40 (@)	$50 (P)	$20 (Space)